2018 Past Paper Question 3
The following is an embedded system scenario for the refrigeration controller consists of a PIC18 micro-controller, a control panel with 3 buttons and 2 LED’s, an analogue temperature sensor, a variable-speed compressor (driven by a BLDC Inverter), and a Bluetooth serial replacement unit operating at 300 baud with 8 data bits, no parity and 1 stop bit.

System Input:
- Compressor Fault Signal (Fault/No Fault)
- BLDC Hall Effect sensors (3-bit pattern - A, B, C)
- Control Panel Buttons - momentary (3-bit pattern - Start/Stop, SP+, SP-)
- Temperature Sensor (continuous value from 0 - 9 degrees Celsius)
- Serial Port Rx (receives ASCII characters at 300baud, 8N1)

System Output:
- Control Panel Operating Light (On/Off)
- Control Panel Alarm Light (On/Off)
- BLDC Motor Switching Pattern (6-bit pattern); motor response time 10 ms
- Serial Port TX (transmits ASCII characters at 300 baud, 8N1)

System Resources:
- R1 Mutex associated with global variables Running, Temperature Error and Setpoint
- S1 Semaphore associated with Compressor Faults, maximum value
- TXQ Message queue containing characters for transmission via Bluetooth
- RXQ Message queue containing characters received via Bluetooth

Task 1 – BLDC Control
Controls PWM signals for compressor; Runs at 100 ms intervals if global boolean variable Running is TRUE.

J11, e=10ms if Running == TRUE then release J12 and J13
J12, e=5ms from J11, set Operating Light ON;
J13, e=10ms from J11, if Compressor Fault Signal == TRUE then generate S1 else release J14 and J15
J14, e=5ms from J13, lookup BLDC Motor Switching Pattern based on BLDC Hall Effect Sensor Pattern
J15, e=15ms from J13, acquire R1; set PWM Duty Cycle based on Temperature Error; release R1

Task 2 – Temperature Monitor
Reads Temperature Sensor; Runs at 0.5s intervals; local static variable Temperature.

J21, e=10ms Update Temperature reading
J22, e=10ms after J21, if Temperature exceeds 4 C then put ‘*’ on TXQ
J23, e=10ms after J21, acquire R1; calculate Temperature Error = Temperature - SetPoint; release R1

Task 3 – Interface Control
Serial Communication + User Interface; Runs at 1s intervals. Phase Delay 0.25s; local variable p.

J31, e=20ms If Start/Stop Button was pressed THEN Acquire R1, Running = ! Running, Release R1
J32, e=20ms if SP+ button was pressed THEN Acquire R1, Setpoint++, Release R1
J33, e=20ms if SP- button was pressed THEN Acquire R1, Setpoint–, Release R1
J34, e=15ms Consume S1 (5ms timeout) - If consumed Alarm Light = ON
J35, e=30ms if TXQ is not empty, and TX is IDLE, get character from TXQ and place in TXChar
J36, e=30ms If RXQ is not empty, retrieve p from RXQ, if p is between ‘0’ and ‘9’ THEN Acquire R1,
Setpoint = p-‘0’, Release R1

ISRHandler – Serial Communication
Manages TXQ and RXQ; Runs on demand - baud rate 300, 8 data bits, no parity bit, 1 stop bit.

Jisr1, e=2ms if Rx Interrupt, Add RXChar to RXQ
Jisr2, e=2ms if TX Interrupt, get character from TXQ and place in TXChar

Question A
Based on the embedded system scenario specified earlier with real time requirements where the jobs and tasks for such system are described.
Construct a cyclic executive schedule for the execution of tasks 1 to 3 where the minor cycle is 50ms. You should presume that interrupts are never disabled.

Question B
Based on the embedded system scenario specified earlier with real time requirements where the jobs and tasks for such system are described.
Construct and graph an appropriate task timelines for the execution of these jobs assuming that they are scheduled using a time-based task manager with a 100ms tick, where blocked tasks will trigger a context switch to the next ready task, and each tick the next ready task in the queue is allowed to run. You should presume that interrupts are never disabled.

Question C
Based on the embedded system scenario specified earlier with real time requirements where the jobs and tasks for such system are described.

Compare the task performance achieved using the cyclic executive, and the time-based task manager. Your answer should clearly identify at least three criteria you could use for comparison, and explain which system you would prefer to implement on the basis of those criteria.

Question D
Based on the embedded system scenario specified earlier with real time requirements where the jobs and tasks for such system are described.

You are told that Job J15 has a relative deadline of 50 ms after the release of Task 1. Use a precedence graph to determine the effective task deadlines of the jobs in Task 1, and indicate the order in which Task1 jobs would run if the Deadline Monotonic priority-assignment algorithm was used on the effective deadlines.

Question E
Based on the embedded system scenario specified earlier with real time requirements where the jobs and tasks for such system are described.

Identify three potential hazards/risks that the system may present, if implemented using pre-emptive priority-based scheduling, where Task 1 has the highest priority, Task 3 has the lowest priority, and interrupts are never disabled. Suggest mitigating strategies for each hazard/risk.